## Slide 1: Production and counting of uncontained sources in SNO
Simon JM Peeters

## Slide 2: Content
The SNO experiment
  Calibration of the SNO experiment
Production of 222Rn and 24Na sources
Distribution of uncontained radioactive sources
Conclusions
Registered at this conference
Notes: 17 pages article, representing a significant amount of work from 33 (SNO) authors, 16 registered at this conference.
Describes the production and counting of distributed sources of 24Na and 222Rn in the Sudbury Neutrino Observatory (SNO).
These are unique sources that have provided accurate calibrations of the response to:
- Neutrons (response He3 counter array)
(produced through photodisintegration of the deuterons in the heavy water target)
low energy betas and gammas (response of background Cherenkov light from trace amounts of natural radioactivity)
Although these sources were unique to SNO, we feel similar techniques could be extremely useful for the calibration of future low background detectors.

## Slide 3: The sudbury neutrino observatory
Part I

## Slide 4: Sudbury Neutrino Observatory
Located here @ 5890±94 mwe
1 ktonne ultra-pure D2O target inside 12 m diameter acrylic vessel
7 ktonnes ultra-pure H2O shielding
Cavity with urylon liner
Nitrogen blanket
9456 inward + 91 outward 10” PMTs with light concentrators (54% coverage) on 17.8 m diameter support structure
Detector parameters

## Slide 5: Sudbury Neutrino Observatory
Cherenkov light produced by electrons from ES/CC interactions
NC interactions Detection of the neutron via:
  Phase I (2000/2001) Cherenkov light from Compton scattered electrons from gammas produced by neutron capture on D2O
  Phase II (2001/2003)
  Enhanced NC sensitivity (2 tonnes NaCl) Cherenkov light from Compton scattered electrons from gammas produced by neutron capture on 37Cl
  Phase III (2005/2006) Array of 3He proportional counters
Physics signal

## Slide 6: Summary of SNO calibration (i)
Response to signal-like events
Point sources, a.o. :
  16N 6.1 MeV gamma, ~5 MeV Compton scattered electron
  AmBe, 252Cf
Analytic and MC methods to interpolate between points Very difficult in phase III

## Slide 7: Summary of SNO calibration (ii)
Response to background-like events
Ex-situ techniques assay D2O and H2O
In-situ techniques low energy window (4-4.5 MeV)
β-γ gammas from 208Tl (232Th) and
214Bi (238U chain) can photo-disintegrate
the deuteron
Notes: We have parameterised the mean angle and used in the in-situ analysis to distiniguish between U/Th in the same way it was used in the SNO analysis.

## Slide 8: Use of uncontained sources in SNO
Signal (24Na)
Response of the 3He proportional counters making up the Neutral Current Detector array.
Precise determination of the neutron capture of the Neutral Current Detector array
Backgrounds (222Rn and 24Na)
Calibrate the response of the detector electron equivalent energy and isotropy
Helped with the determination of the detector response to light from the H2O
222Rn: : T1/2=3.82 d, part of 238U chain
24Na: T1/2=15 hrs, pd (2.754 MeV gamma), 232Th-like (1β,2γ)

## Slide 9: Source production
Part II

## Slide 10: 222Rn Production
Extraction from mine air (D2O)
Mine air 100 Bq/m3
Pass to NaOH filters to remove CO2 and a -85 C trap to remove water vapour
Cryogenic trap, counted in Lucas cells
Dissolved in water
Samples counted using ex-situ assay methods
From 226Ra (H2O)
Commercial Pylon source
N2 carrier gas (no CO2)
Marinelli beaker for activity measurement on Ge detector
No Ra: checked by bubbling carrier gas through water and assay the water
~100 Bq
~50 kBq

## Slide 11: 24Na production
Th source (SNO phase II)
330 kBq Th source(2.6 MeV gamma)
inside the fiducial volume SNO (D2O +0.2% NaCl)
Activation (SNO phase III)
10% brine (from phase II)
SLOWPOKE-2 (Royal Mil. Coll, Kingston) 3.75 ml, 20 min, 5x1011 n cm2 s1
Injected into 2.5 l D2O
Pumped into vessel using calibration manipulator
Phase III activity measurements
Sample on carefully calibrated and checked using a Ge detector
Delrin can with sample in the centre of the detector compared to 252Cf source at the same location:
  PMT array
  NCD array
Notes: 1 in 456 gammas produced a neutron. One in 73 neutrons produced 24Na.

## Slide 12: MIXING SOURCES INTO SNO
Part III

## Slide 13: Early mixing studies
SNO recirculation systems used to distribute the radio-activity
Hard to predict exact water movement:
  Low viscosity D2O
  Movement of source
  Temperature difference of injected and target water
Volume weighted nr of events
Th activation data
Notes: Recirculation: 150 l/min
Top half mixes quickly (135 m3 moved in first 15 hours, top half mixed)
Stratification: layer moving down

## Slide 14: Mixing in SNO phase III
First spike:
Based on evidence, inject
along z, most in the bottom.
Mixed after 70 hours.
24Na injection data
Second spike:
inject 1-3 C warmer spike at the bottom. Induced rotation of the bulk, reverse circulation. Mixed after 50 hours.
Notes: We used different, significant ways to establish mixing – for example, it was observed the rate of the NCDs had been very stable before we declared it to be absolutely mixed.

## Slide 15: Conclusions
I have discussed the production and application of distributed 24Na and 222Rn sources in SNO
These techniques have been very useful in the determination of the neutron detection efficiency and response of to natural radiation for SNO
Similar techniques could be useful for future low-background detectors

## Slide 16: FIN

## Slide 19: U/Th decays

## Slide 20: Event Isotropy

## Slide 21
SNO programme
1998
1999
2000
2001
2002
2003
2004
2005
2006
Comm.
D2O
D
2
O
Salt
(NaCl)
Phase I
Phase II
3He Counters
Phase III
γ
γ
γ
35Cl
36Cl
36Cl*
n
n captures on deuterium
σ = 0.0005b
6.25 MeV γ
n captures on chlorine
σ = 44b
8.6 MeV multiple γs
n captures on 3He prop. counter array
σ = 5330b
0.764 MeV
n + 3He  p + 3H
p
3H
5 cm
n
3He
γ
2H
3H*
n
3H